## Slide 1
Light
Microscopy
Lesson Plan
by Sharyn A Endow, PhD
Duke University 2016

## Slide 2
Light
Microscopy
Lesson Plan
Copyright © 2016 by Biophysical Society. All rights reserved.
Notes: This slide presentation was created to accompany the Biophysical Society BASICS Lesson Plan on Light Microscopy.

## Slide 3: References
Gall, J. Early History of Microscopy
http://www.ibiology.org/ibioeducation/taking-courses/early-history-microscopy.html
Nikon Microscopy U.
http://www.microscopyu.com
Optical Microscope, Wikipedia
https://en.wikipedia.org/wiki/Optical_microscope
Slayter, E.M. 1970 Optical Methods in Biology
John Wiley & Sons
Notes: Here are some useful references for further information.

## Slide 4: Microscopes
Microscopes enlarge or magnify objects so details can be seen more clearly
Simple Microscopes consist of a lens, stage and focusing mechanism
Compound Microscopes contain an additional lens or lenses
Notes: Microscopes are used to see objects that are too small to see with the unaided eye. Light microscopes use natural light (sometimes called “white light”) to illuminate the object. Simple light microscopes consist of a lens, a specimen holder or stage, and a focusing mechanism. Compound light microscopes have an additional lens (or lenses) in the eyepieces that magnify the image from the lens (or set of lenses) near the specimen.

## Slide 5: Small Wooden Microscope
Simple
Microscope
Single lens
Stage
Focusing gear
Gift from Echo Laboratories & Chroma Technology Corp to the BPS
Notes: Your small wooden microscope is a simple light microscope. It consists of a lens, specimen stage, and focusing gear to move the stage and focus the specimen. The wooden microscopes used in this slide presentation are a gift from Echo Laboratories and Chroma Technology Corp to the Biophysical Society. The microscopes are available from Echo Laboratories at http://echo-labs.com/woodenscope for US $10, including shipping.

## Slide 6: Lens
Lenses collect and refocus light forming an enlarged image
A focused image is produced when the object is at the lens focal point
Notes: Light microscopes use a lens to enlarge or magnify an object or specimen. Lenses collect light reflected from an object and refocus it at a different plane, forming an enlarged or “magnified” image of the object. Lenses focus light reflected from a point on the object at a given distance or focal length from the lens. If you place an object at the focal point of the lens, the object will appear sharp when you view it through the lens. Focusing a specimen under a microscope means to move it into a position close to the focal point of the lens. For the small wooden microscope, moving the stage up and down will focus the specimen by changing the distance of the specimen from the lens until its height is close to the focal length of the lens.

## Slide 7: Magnification
Magnification is the enlargement of an object produced by a lens relative to its ACTUAL size
M = SF / SA
M is magnification
SF is the final specimen size
SA is the actual specimen size
Notes: Magnification refers to the enlargement of the object by a lens. Your small wooden microscope has a lens that magnifies objects by less than ~2-3 fold. If you examine an object by placing your cell phone over the microscope lens and look at the object through the camera viewer, you are using the lens in your cell phone camera to magnify the object further. This converts the simple wooden microscope into a compound microscope!

## Slide 8: Spherical Aberration
Imperfect lenses distort light at the edges, causing spherical aberration
Images appear distorted due to multiple images of the object rather than only one
Notes: If you look carefully at a specimen through your small wooden microscope, you can see a difference in the sharpness of focus and size of the specimen at the edges and center of the lens – this is caused by spherical aberration. Modern microscopes have lenses that are corrected for spherical aberration by blocking the light at the edges, producing an image only with the center of the lens; by adding another lens that has the opposite effects on the bent light at the edges, bringing it into focus with the light at the center; or by altering the lens at the edges using special lens-grinding methods to correct for spherical aberration.

## Slide 9: Assembling Your Wooden Microscope
Parts #1-6 form the focusing gear
Partially assembled gear :
Assembled gear:
Notes: The microscope comes as a ready-to-assemble kit and can be assembled in a few minutes after viewing the video instructions at the Echo Laboratories web site at http://echo-labs.com/woodenscope There are 19 pieces in the wooden template. First, carefully release the pieces from the wooden template, keeping track of their part numbers - a small flat spatula can be helpful in releasing the pieces. Parts #1-6 form the wheel-like gear that moves the stage up and down to focus the specimen: parts #2, 3, 4 & 5 fit onto the end of part #1 (in that order) to form the gear and part #6 holds it on the end of part #1. Note that part #3 fits inside part #4 and that part #4 in the assembled gear should rotate freely. The pieces fit together in a “lock-and-key” fashion, much like Legos.

## Slide 10: Assembling Your Wooden Microscope
Part #10 is the stage and sits on the arms of parts #8 & #9; it fits into the slot at the center and notches made by #8 & #9
Finished stage:
Parts #7-12 form the stage piece
Parts #8 and #9 fit onto the sides of part #7:
Parts #11 & 12 fit onto part #7
Notes: Parts #7-12 form the stage piece (part #10 is the stage itself) and back (part #7) into which the focusing gear fits; parts #8 and #9 attach the stage to the back. The small parts #11 and #12 position the bottom of the stage back at the sides – they fit in the indents below the square holes, facing inwards. All of the parts should “click” into place.

## Slide 11: Assembling Your Wooden Microscope
Part #14 fits over the stage, lens curved side down
Parts #13 and #19 are the sides
Notes: Parts #13 and #19 are the sides. First position the assembled focusing gear and stage, and the lens holder (part #14) into the slots in part #13. Note that the rounded side of the lens should face down when it is properly positioned in the lens holder. If the lens falls out, place it flat side down on a piece of paper, then place the round hole of part #14 over the lens and push down gently on either side – the lens will seat itself in the hole and you can continue with the microscope assembly. After fitting the lens holder, stage, and focusing gear into the slots in part #13, carefully position and fit part #19 into place - note that there are 4 notches that fit into slots of part #19. If they do not fit easily, wiggle them a little to see if the fit is better. In the slide above, part #14 fit better upside down (with the Echo/Chroma logo facing down, rather than facing up; the lens was repositioned so the curved side was down).

## Slide 12: Assembling Your Wooden Microscope
Finished!!
Parts #16 and #18 fit across the top
Part #17 fits across the bottom
Part #15 fits over the lens
Notes: Turn the microscope upright and fit part #15 into place over the lens held by the side notches. Part #16 fits across the top next to part #15 and part #18 fits across the top at the back to hold the sides together. Part #17 fits across the bottom to hold the sides together. Note that the direction in which parts #16 and #18 point is not important – they can be fit so that the overlap is to the left or right of the microscope, as you face the stage. After assembly, make sure that all the parts fit securely into their slots. The microscope should be sturdy and stay together when you move it – if not, try gently pressing the sides together again, along with the top and bottom. The stage should move up and down when you turn the focusing wheel, and stay fixed in place at intermediate positions.

## Slide 13: Testing Your Wooden Microscope
Find the image of Abraham Lincoln on a US penny
Viewed by eye Viewed on a small wooden microscope
Magnification, ~16X
Notes: Look at a US one-cent coin, or penny, to test your new microscope. The image at the left, taken without the microscope, shows the Lincoln Memorial on the back of a penny. The image on the right was taken through the lens of a small wooden microscope (region in green dashed box in image at the left); it shows a seated figure – Abraham Lincoln! The seated figure is difficult to see without the microscope.

## Slide 14: Using Your Wooden Microscope
Viewed on a small wooden microscope
Viewed by eye
Notes: The image at the top left shows a variegated plant leaf with regions of green, pink and pink-white, which can be easily seen without a microscope. The images at the bottom left and right, taken through the lens of a small wooden microscope, show that pink and pink-white cells are unevenly distributed near the green cells. There are also tiny hairs along the edge of the leaf that cover the entire surface of the leaf – these cannot be easily seen without a microscope.

## Slide 15: Using Your Wooden Microscope
Viewed by eye Viewed on a small wooden microscope
Notes: At the left is a lichen, growing on a piece of tree bark, which has curly leaves that can be seen without a microscope. The leaves have bristles at their edges, which go unnoticed if the lichen is not examined under a microscope.

## Slide 16: Using Your Wooden Microscope
Viewed by eye Viewed on a small wooden microscope
Magnification, ~18X
Notes: At the left is a fruit fly imaged without a microscope and at the right, another fly of the same size visualized through the lens of a small wooden microscope. The red eye and dark abdomen at the end of the fly can be seen in the photo taken without the microscope. They are clearly observed in the photo taken through the lens of the microscope, together with the yellowish color of the abdomen (top, yellow arrow). The thoracic bristles (right, yellow arrow) and wing veins (bottom, yellow arrow) are also clearly visible.

## Slide 17
Light
Microscopy
Lesson Plan
Copyright © 2016 by Biophysical Society. All rights reserved.
Special thanks to Echo Laboratories & Chroma Technology Corp for a gift to the Biophysical Society of small wooden microscopes
Notes: This slide presentation is available on the Biophysical Society web site at http://www.biophysics.org/BiophysicsWeek/Resources/tabid/6654/Default.aspx